## Slide 1: Authentication with 802.1X. Wireless networking concepts
Lecture 5
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Authentication with 802.1X
Wireless networking concepts
Demonstration

## Slide 3
Authentication with 802.1X

## Slide 4: AAA
AAA: Authentication, Authorization and Accounting
    Authentication – “Who are you? Prove it!”
    Authorization – “This is where you have access and where you do not”
    Accounting – “I am recording all (un)successful login attempts”
Often a single server plays the three roles but can be multiple servers as well

## Slide 5: 802.1X
IEEE 802.1X is an IEEE Standard for Port-based Network Access Control (PNAC)
Part of the IEEE 802.1 group of networking protocols
Provides authentication mechanism to devices asking to attach to a LAN or a WLAN
Uses Extensible Authentication Protocol (EAP) over LAN – known as EAPOL

## Slide 6: The participants in 802.1X
Supplicant - the end device requesting access
Authenticator – usually a switch or AP which is to provide access
Authentication Server - the device which makes the decision (grant/deny access) Usually RADIUS server

## Slide 7: 802.1X

## Slide 8: Why 802.1X?
The switches and access points do not need to know how to authenticate the client
They (authenticators) simply pass the authentication information between the client and the authentication server
That is why it is easier for 802.1X to support many authentication methods

## Slide 9: 802.1X and EAP
802.1x uses EAP to facilitate the communications between the participants
Common EAP authentication types:
  EAP-MD5 - minimal security, one-way authentication
  EAP-TLS - mutual authentication, secure but no very easy to adopt
  EAP-TTLS - mutual authentication (optional client certificate)
  EAP-PEAP - most popular method, has an “outer” and “inner” methods, developed by Cisco, Microsoft and RSA Security

## Slide 10: Network Access Protection

## Slide 11
Wireless networking concepts

## Slide 12: Cable vs Wireless?
Speed
Signal quality
Mobility
Device adaptability
Security
Interference

## Slide 13: 802.11 standards
IEEE Standard | 802.11b | 802.11a | 802.11g | 802.11n | 802.11ac | 802.11ax
Friendly name | WiFi 1 | WiFi 2 | WiFi 3 | WiFi 4 | WiFi 5 | WiFi 6
Year adopted | 1999 | 1999 | 2003 | 2009 | 2014 | 2019
Frequency | 2.4 Ghz | 5 Ghz | 2.4 Ghz | 2.4/5 Ghz | 5 Ghz | 2.4/5 Ghz
Max data rate | 11 Mbps | 54 Mbps | 54 Mbps | 450 Mbps | 1.7 Gbps | 2.4 Gbps
Typical range indoors* | 35 m | 35 m | 38 m | 70 m | 35 m | -
Typical range outdoors* | 140 m | 120 m | 140 m | 250 m | 250 m | 250 m

## Slide 14: SSID
SSID: Service Set Identifier
This is the name of the wireless network (not the Access Point name)
It is up to 32 characters in length
A single AP can broadcast multiple SSIDs
Should you hide your SSID?

## Slide 15: Wireless security
Hiding the SSID (“not the best” security)
MAC ID filtering
Static client IP addressing
802.11 security (next slide)

## Slide 16: 802.11 security
WEP - very weak, deprecated
WPA - better than WEP, still risky
WPA2 - the de facto standard
  WPA2 (TKIP) - risky
  WPA2 (AES)
  WPA2-PSK vs WPA2-Enterprise (which uses EAP)
  WPA3 - improved general Wi-Fi encryption
  WPA3 - personal (uses Simultaneous Authentication of Equals (SAE) vs PSK)
  WPA3 - enterprise (targets large-scale Wi-Fi with optional 192-bit security)
Better security

## Slide 17: Wireless devices management
APs in standalone mode
APs controlled by a controller

## Slide 18
Corporate WEB and DNS Server
g0/1
g0/2
ge1/0/25
ge1/0/27
ge1/0/26
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
fe0/0/0
fe0/0/1
SSID:
NetFund-Corporate
SSID:
NetFund-Guest

## Slide 19
Demonstration

## Slide 20: Summary
…
…
…
Authentication with 802.1X
Wireless networking concepts
Demonstration

## Slide 22: SoftUni Diamond Partners

## Slide 23: Educational Partners

## Slide 24: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 24