## Slide 1: Software Defined Networking
Lecture 8
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Traditional networking
Software Defined Networking (SDN)
Simulators for SDN
Demonstration

## Slide 3
Traditional networking

## Slide 4: The old (current) way of doing networking
Networking vendors sell proprietary hardware
Hardware can be different, but devices talk to each other using protocols
These protocols are built in the OS/image in each device
We need to separately configure the logic for each “box” by using:
  Command Line Interface (CLI)
  Some kind of Network Management System (NMS)

## Slide 5: How network devices make forwarding decisions
Switches and routers should decide where to send a particular packet so each device may need to consider, build or change:
  MAC address tables
  Routing tables
  Use ARP to find the destination MAC
  Decrease the TTL of each packet
Different planes on each device are responsible for the different tasks: control plane, data plane and management plane

## Slide 6: Devices and planes
Control plane (the brain). Responsible for:
  Building ARP tables
  Building routing tables
  Running STP to avoid loops
Data plane (the muscles). Responsible for:
  Encapsulation/decapsulation
  Adding or removing headers (802.1Q for example)
  Replace source/destination address (if there is NAT)
Management plane - used for accessing and managing the devices. Examples - Telnet, SSH

## Slide 7: The control and the data planes

## Slide 8: Limitation of traditional networking
When adding a new service/server in the network, this may lead to creating and configuring:
  VLAN
  STP
  Subnet
  Routing
  Firewall rules (ACL)
  Etc…
The whole process is slow, manual and may lead to configuration errors

## Slide 9
Software Defined Networking (SDN)

## Slide 10: What is SDN?
SDN - Software Defined Networking
SDN uses a centralized control plane - SDN controller

## Slide 11: SDN controller interfaces
Northbound Interface (NBI)
  Used to access and program the controller
  Can have GUI, CLI and API
  You can write scripts for automation
Southbound Interface (SBI)
  The controller’s communication with the “dumb” devices
  It is a software interface, often API

## Slide 12: SDN northbound interface
The interface allows multiple applications to access the controller:
  GUI
  Java/Python or other scripts
  3rd party apps
REST API (next slide) is typically used

## Slide 13: REST API
REST - Representational State Transfer
REST API uses HTTP messages to send and receive information between SDN controller and another application
Examples for such messages:
  HTTP GET: used when we want to retrieve information
  HTTP POST/PUT: used when we want to upload or update information
  The two most used data formats are:
  JSON (JavaScript Object Notation)
  XML (eXtensible Markup Language)

## Slide 14: SDN southbound interface
This is the controller’s communication with the “dumb” hardware
It specifies a software (not a physical) interface
Some popular southbound interfaces:
  OpenFlow
  Cisco OpFlex
  CLI (in the APIC-EM controller)

## Slide 15: SDN OpenFlow

## Slide 16
Simulators for SDN

## Slide 17: Mininet and miniedit
What you need:
  Mininet image
  Virtualization software, for example VirtualBox
  Terminal emulator software, for example PuTTY
  X11 display server, for example Xming
  sudo ~/mininet/examples/miniedit.py
  Patience…

## Slide 18: Mininet and miniedit (2)

## Slide 19: HPE VAN SDN controller and Mininet
What you need:
  HPE VAN SDN controller appliance
  Mininet image
  Connectivity between both VMs and the host
  Browse to the controller: https://ip_address:8443/sdn/ui (user: sdn, password: skyline)
  Login to Mininet and type: sudo mn --controller=remote,ip= --topo=linear,4 --mac

## Slide 20: HPE VAN SDN controller and Mininet (2)

## Slide 21: Cisco APIC-EM
APIC-EM: Application Policy Infrastructure Controller - Enterprise Module
Created to be used with existing hardware
Uses REST API for the northbound interface
Uses common protocols, like SNMP, Telnet, SSH, for the southbound interface
Can be installed from an iso image
There are labs which does not require local installations

## Slide 22: Cisco APIC-EM (2)

## Slide 23: VMWare NSX
NSX is network virtualization platform, which provides:
You can try the VMware NSX Data Center for free (enable browser pop-ups)
Logical switching | Logical load-balancer
Logical routing | Logical VPN
Logical firewall and NSX gateway | NSX API

## Slide 24
Demonstration

## Slide 25: Summary
…
…
…
Traditional networking
Software Defined Networking (SDN)
Simulators for SDN
Demonstration

## Slide 27: SoftUni Diamond Partners

## Slide 28: Educational Partners

## Slide 29: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 29